## Slide 1
SOLUTION PRESENTATION
SENTINEL / GUJARAT
01
Every alert earns
its confidence.
A working single-host pilot for camera onboarding, vehicle and plate analysis, governed face matching, route plausibility, and reviewable evidence.
RUNNABLE PILOT
HONEST EVIDENCE
Notes: Lead with the decision quality thesis. The product is runnable locally; live detector inference needs Docker Desktop and a permitted feed. Synthetic scenario data is labelled throughout.

## Slide 2
01 / PROBLEM
SENTINEL / GUJARAT
02
The camera estate is a decision problem
A useful system must turn heterogeneous streams into defensible operator actions.
80,000+
camera scale in the brief
~160 Gbit/s
at 2 Mbit/s each, before overhead
Fragmented sources
Different departments, protocols, and vendors hide context.
Uncertain reads
Single-frame OCR can turn a weak crop into a confident claim.
Alert fatigue
Matches need context, an explicit review path, and provenance.
Cost of central video
Continuous backhaul is the wrong unit of scale; move metadata.
Notes: 80,000 is from the supplied plan, not measured capacity. Bandwidth arithmetic assumes every camera sends 2 Mbit/s continuously.

## Slide 3
02 / ARCHITECTURE CHOICE
SENTINEL / GUJARAT
03
Hybrid by design
One registry and operations view; analysis can move to district or site edge.
CAMERA & NVR
RTSP / RTMP / HLS / file
→
EDGE ADAPTER
MediaMTX + frame decode
→
REGIONAL EVENTS
Tracks, plates, face matches
→
COMMAND VIEW
Review, search, export
Current pilot
Single host: FastAPI + PostgreSQL + detector worker + MediaMTX + React
Reference Models 1–5 require the official portal brief for an accurate side-by-side mapping.
Notes: The supplied PDF suggests a hybrid model but is not the official portal. Do not claim a precise comparison against all reference models until portal access is provided.

## Slide 4
03 / DIFFERENTIATORS
SENTINEL / GUJARAT
04
Three mechanisms that reinforce each other
Each keeps weak evidence visible instead of silently upgrading it.
01
Camera Passport
URL or footage onboarding; codec, fps and resolution probed; named department and map point.
02
Route gate
Cross-camera candidates show distance, time gap and implied speed. Impossible jumps enter review.
03
Governed FRS
Enrollment needs authority, expiry, admin entry and separate reviewer approval. Unmatched embeddings are discarded.
Notes: Describe these as implemented mechanisms. An uploaded public traffic sample is available for ingest; the live worker path was not executed because Docker Desktop engine was unavailable.

## Slide 5
04 / IMPLEMENTED SYSTEM
SENTINEL / GUJARAT
05
The working path
A camera becomes a normalized record; a track becomes a reviewable decision.
FEED
URL / video
→
DETECT
YOLO + ByteTrack
→
READ
OCR consensus
→
MATCH
watchlist + gate
→
ACT
alert + export
DATA PLANE
MediaMTX + detector worker
DECISION PLANE
FastAPI + audit + React
Notes: The current worker samples every third frame. Events are sent to FastAPI. MediaMTX supplies browser playback for compatible codecs.

## Slide 6
05 / END-TO-END WORKFLOW
SENTINEL / GUJARAT
06
One vehicle, six accountable steps
The operator can see where the automated chain became uncertain.
01
Onboard
Camera Passport
02
Track
ByteTrack ID
03
Read
Top 3 OCR votes
04
Correlate
Authority + expiry
05
Gate
Distance ÷ time
06
Review
Note + evidence
Notes: Read status can be confirmed, low confidence, or unreadable. The gate is a conservative Haversine/detour approximation, not a road route.

## Slide 7
06 / AI ANALYTICS
SENTINEL / GUJARAT
07
What the model actually does
No accuracy number is claimed until labelled camera footage is tested.
RUNNABLE ANALYTICS
Vehicles → tracks → candidate plate crops → OCR → one observation per track
LOW-CONFIDENCE KEPT
Optional approved face match
YuNet + SFace only compare to approved, unexpired entries.
Future model work
Indian plate detector, labelled recall/read-rate study, and the brief’s remaining event analytics.
Notes: Vehicle model is YOLO11n. Optional plate YOLO weights can be supplied. Baseline plate proposals use contours with Tesseract. Do not claim six event types are implemented.

## Slide 8
07 / WATCHLIST + ALERTS
SENTINEL / GUJARAT
08
A hit is a structured claim
Identity, authority, expiry, confidence and route context travel together.
MATCH
Exact plate / fuzzy plate / approved face
GATE
Plausible / impossible / insufficient history
TRIAGE
P1 action / human review / reject from action
EVIDENCE
Snapshot hash / model / audit digest
Notes: The local deterministic score stays in code. No Jev API or external triage model is presented as implemented.

## Slide 9
08 / PRODUCT PROOF
SENTINEL / GUJARAT
09
The impossible jump goes to review
One deterministic synthetic run; scenario counts are not field metrics.
ALERT CARD / DEMO
GJ01AB1234
GATE REJECTED
Sarkhej Junction · stolen
Impossible travel in 8 seconds → review queue
09
tracks
07
matched alerts
02
rejected routes
These are scenario counts, not measured field accuracy or false-alert reduction.
Notes: One run creates nine synthetic tracks, seven alerts and two route rejections. This is integration proof only. The camera-wall Delhi replay clips are visual placeholders, not the source of Ahmedabad event records. No government feed or owned footage was available.

## Slide 10
09 / TECHNOLOGY
SENTINEL / GUJARAT
10
Self-hostable core, explicit licensing
The video and decision path can run on a local machine.
Stream
MediaMTX
MIT; localhost-bound pilot
Analytics
YOLO11n + ByteTrack
Ultralytics AGPL / commercial option
OCR + face
Tesseract + OpenCV Zoo
Model and data rights to verify
Data + API
PostgreSQL/PostGIS + FastAPI
Local storage, JWT roles
Console
React + Vite
OpenStreetMap tiles online
Compose defines a reproducible local pilot. Docker engine was unavailable during this verification.
Notes: Do not claim production license clearance. The README names the model caveats and optional Indian plate weights.

## Slide 11
10 / SCALING DESIGN
SENTINEL / GUJARAT
11
Move events, not every frame
A state deployment is an architecture proposal, not a benchmark result.
160
Gbit/s
80,000 × 2 Mbit/s, continuous central backhaul
SITE / DISTRICT
Ingest, analytics, short video retention
REGION
Replayable metadata bus, routing and storage
STATE
Federated registry, search and command view
Notes: Production requirements include durable event bus, PostGIS indexing, GPU sizing, credential rotation, clock-health checks, object storage, and SSO. None was load tested.

## Slide 12
11 / GOVERNANCE
SENTINEL / GUJARAT
12
Built for accountable operators
Each decision can be inspected, reversed, and attributed.
Role gates
Operator, administrator and independent face reviewer.
Two-person face approval
Authority and expiry attached before a face entry becomes active.
Audit chain
Each material action includes prior digest; verifier locates tampering.
Evidence packet
PDF includes source label, model, snapshot digest, audit digest.
Pilot caveat: localhost network boundary; no external audit anchor or signed forensic seal.
Notes: The pilot has not been independently security audited. Native media URLs carry a JWT query parameter for local preview; protect gateway and media routes before network deployment.

## Slide 13
12 / DEPLOYMENT PATH
SENTINEL / GUJARAT
13
From pilot to department trial
A useful trial starts with authorized sources and labelled evaluation clips.
NOW
Local pilot
Synthetic scenario and public ingest clip.
→
NEXT
Department trial
2–3 departments; approved feeds, GPS, clocks, watchlists.
→
THEN
District scale
Edge workers, durable bus, retention and SSO.
→
LATER
State scale
Partitioned search, capacity tests, operating model.
Notes: Required department inputs: inventory, GPS, protocol, VMS/API access, NAT/VPN/bandwidth, NTP, watchlist legal authority, retention, export policy and named approvers.

## Slide 14
13 / EVIDENCE + NEXT GATE
SENTINEL / GUJARAT
14
Prove impact with the next real feed
The product is ready to evaluate; field performance remains unmeasured.
VERIFIED IN THIS BUILD
• API integration tests pass
• Frontend production build passes
• Camera upload and playback checked
• Scenario alerts, route and exports checked
• Face model loading checked
MEASURE ON AUTHORIZED FOOTAGE
• Exact plate read rate
• Vehicle recall
• False alerts before / after gate
• p50 / p95 frame-to-alert latency
• Clock and camera health
Submission status and portal eligibility require organizer confirmation; public notice lists 15 Sep 2026 as the original deadline.
Notes: Do not present a synthetic run as a government feed demo or as measured field impact. Ask organizer whether the round is open.